ST.STEPHEN'S COLLEGE PATHANAPURAM

(Affiliated to the University of Kerala)

Maloor College P.O., Pathanapuram, Kollam (Dt.)

Kerala-689 695 Tel: 0475-2352385/2354385/23514(O)

E-mail: ststephenspathanapuram@gmail.com

Website:www.ststephenspathanapuram.ac.in

List of Equipment’

Category I

CATEGORY I

| Sl No | Instrument | Technical Specifications | Quantity | Rate |
| --- | --- | --- | --- | --- |
|  | HOT AIR OVEN | Hot air ovens are sturdy double walled units Inner chamber made of SS/Alu and outer made of mild steel with power coating Gap between the walls filled with glass wool insulation to avoid heat loses.Temp.is controlled by thermostat. Temp 50ºC to 250C and accuracy +-1C air ventilators are placed on top of both sides to remove hot gases.fumes. Chamber Size 600x600x600 Mm, No of Trays-03, Watts- 1055, Ltr approx.-225 | 1 |  |
|  |  | Microprocessor based digital temperature controller instead of thermostat | 1 |  |
|  |  | Air circulation fan | 1 |  |
|  | BOD INCUBATOR | For BOD test storage of sensitive cultures, vaccines etc culture of bacteria microorganism and plant life; serum incubation studies and immunological work etc. Provided illumination inside the working chamber with the help of CFL. Double wall construction, inner madeof SS and outerM.S , Powder coated with adjustable trays. CFC free refrigeration and heating system with powerful Air circulation for creating positive airflow throughout the working chamber. The unit has a temperature range from 5 0C to 600C with an accuracy of +/-0.50C. Volume- 275 Ltrs,Inner chamber- 570 x510 x 1200 mm Capacity- 10 Cft, No of shelves | 1 |  |
|  | HEATING MANTLE | 500ml | 1 |  |
|  | DIGITAL HOT PLATE WITH STIRRER | 10 Ltr magnetic Stirrer with ceramic coated stainless steel plate Speed Range /Control : 0 to 2200 RPM Time Range : 1 to 999 minutes & continuous Ceramic Coated Stainless Steel Plate Room Temperature to 320 deg C Temperature control : 1deg C /step 600W Heat Output Set-up plate dimensions : 140 mm Permissible ambient temp. / humidity: 5 - 40°C, 80% RH Input Voltage : 200 / 240 VAC Power consumption : 610W | 1 |  |
|  | ELECTRIC BUNSEN WITH ENERGY REGULATOR | Stainless steel casing - conical refractorycup - maximum temperature 800°C to 1000°C Watts 350W | 3 |  |
|  | WATER BATH RECTANGULAR (DOUBLE WALLED -THERMOSTATIC CONTROL) | Temperature range from ambient temperature to 100˚C Thermostatic control with an accuracy of + 1°C. Double walled inside of Stainless Steel 304 quality and outside of mild steel duty powder coated. Top of the Bath and concentric rings are made of Stainless Steel. To work on 220/230 volts A.C. with on/off switch, cord. pSliuzge: 350 x 400 x 100mm , 12 HOLES , 75mm dia OPTIONALS AT EXTRA COST: Digital electronic microprocessor based temperature controller cum indicator in the place of thermostat. | 1 |  |
|  | OIL FREE PORTABLE VACUUM PUMPS (DIAPHRAGM TYPE) | Oil free portable vacuum cum pressure pump. Portable diaphragm type vacuum pumps cum oil free air compressors manufactured from special grade aluminium for light weight andstrength, Built in Micro Suction Filter. Diaphragms are made of 2-pay nylon reinforced neoprene rubber and valves are of SS316 with special sealed bearings thus eliminating lubrication. Extremely useful as vacuum pumps in laboratories, filtration instruments, gas charging suction and labeling machines, etc. Equally useful as a compressor in flame photometers, spectrophotometers, nebuliser, laminating press, plastic welding, oil-free spray painting, agitation, etc. Max. Flow (lts./min) : 45 "Max. Vacuum (in. Hg) : 27"" Max. Press (Psig) : 60 Motor HP : 1/4" | 1 |  |
|  | REFRIGERATOR | LG Refrigerator single door 190 ltr 4 star single door ,frost free | 2 |  |
|  | MICROTOME | Feed Adjustment 1-50 microns in step of 1 micron each. Packed in Cardboard Box with one razor,120nm, Three object holders Dust cover and oil can bottle | 1 |  |
|  | DISPOSABLE BLADE | Microtome blade kit for Model MT-1090A | 1 |  |
|  | TISSUE FLOTATION BATH | Double wall, inside made of Alu; and outer made of M.S. Sheet with duly Powder coated. Temperature is controlled from ambient +5°C to 80°C by imported Thermostat /Energy Regulator and without thermometer.200mm x90mm | 1 |  |
|  | PARAFFIN EMBEDDING BATH | Double walled, inner made of SS 304 quality sheet and outer body made of MS duly powder coated. Temperature is controlled by an imported thermostat from ambient +5°C to 80°C with an accuracy of +/- 1°C. The bath is insulated by 25mm glass wool on 5 sides and 6 holes are provided to accommodateSS pots having approx 63mm dia X 65mm depth. | 1 |  |
| CATEGORY II |
|  | COLORIMETER | 8 Filters in a turret covering range from 400 nm to 700 nm; % T ABS, CONC & K Factor Sample volume needed only 300 ul in 1 ml cuvette or 1ml in 4 ml cuvette test tube Accepts round and square test tubes Facility to drop a narrow band interference filter for specific application Hermetically sealed photodiodes adds ruggedness4- digit LED display | 1 |  |
|  | TURBIDITY METER | Accurate and elegant manual instrument Range : 0 – 1 NTU, 0 – 10 NTU, 0 – 100 NTU & 0 – 1000 NTU Readout : 2 digit LED Accuracy: 1.5% of FSD in 0-1 and 0-500 NTU 2% of FSD in 0-1 and 500-1000 NTU Source : LED Detector : Photodiode | 1 |  |
|  | CONDUCTIVITY METER | 7 digit-7 segment LED4 Digit Display for Conductivity 3 Digit Display for Temperature; Conductivity Range: 0.1 S to 100 Milli S in six decade ranges Accuracy:+/1% of FS +/- 1 Digit Minimum Resolution:0.1 S Temp. Compensation: 0.0 to 9.9% per o C Cell Constant : 0.1 to 5.0 CC (Automatic); Calibration in battery back-up memory TEMPCO Analysis Facility Calibration in battery back-up memory TEMPCO Analysis Facility Optional Printer Facility | 1 |  |
|  | HUMIDITY METER | Barigo German 100 mm 0 to 100% R.H. HAIR HYGROMETER | 1 |  |
|  | DIGITAL PHOTOELECTRIC COLORIMETER WITH 8 FILTERS | Min Volume : 1 ml Display : 2 1/2 digit LED Range:400¬700nm Output : 0¬1.99 OD Resolution : 0.01 OD Accuracy : 0.5% FSI | 2 |  |
|  | DIGITAL POTENTIOMETERWITH STIRRER | Digital Potentiometer with mV range 0 to +/-1999V, 1mV resolution, magnetic stirrer with variable control, 3 & 1/2 digit LED display Combined or separated platinum and ref. electrodes stirrer speed control set zero adjustment and hold/ read switch on frontpanel | 1 |  |
|  | pH METER | Meter Type : Benchtop Min pH : (pH) 0 Max pH : (pH)14 pH Resolution : 0.01, 0.1 pH Accuracy : ±0.01 Buffer Recognition : USA, NIST, user defined Calibration : 1 to 3 points Min mV : (mV)-2000 Max mV : (mV)2000 mV Accuracy : ±0.01% full-scale Max Conductivity— Min Temperature : (°C) 0 Min Temperature : (°F) 32 Max Temperature : (°F) 212 Temperature Resolution : 0.1°F/C Temperature Accuracy : ±0.36°F (0.2°C) Temperature compensation : Yes, 32 to 212°F (0 to 100°C), automatic or manual Power (VAC) : 110 - 120 Power (Hz) : 60 | 1 |  |
|  | CONDUCTIVITY METER | Microprocessor based with LED display with following specifications. Range selection: 20 mS to 1000mS, Resolution: +/1mS/cm, Temperature compensation: Automatic 0 to 50 degree C Cell Constant 0.5 to 1.5 adjustable, With all accessories | 2 |  |
|  | ABBE REFRACTOMETER | Refractive Index nD : 1.3000 - 1.7000 Measurement Accuracy : ±0.0002 Dissolved Solids Brix : 0 - 95% "Overall Dimensions : 270 x 180 x 370mm | 1 |  |
|  | VORTEX MIXER | Touch and continuous operations Wide speed range : 0 – 2800 rpm stepless speed regulation Used for various mixing applications with optional adapters, handles upto 48 tubes Aluminium cast base Shaking movement : orbital Orbital diameter :4mm Motor type : Shaded pole AC motor Run type : continuous / touch operation | 1 |  |
|  | DIGITAL MELTING/ BOILING POINT DETERMINATION APPARATUS | With silicon oil Bath of 200 ml & Stirrer With four digit LED display Adjustable heating rate and stirrer speed. Range up to 300°C | 1 |  |
|  | ROTARY SHAKER | The unit has base assembly fabricated from heavy mild steel sections. The drive has a single ex center bearing and heavy duty main bearing resulting in a small number of movingparts. The simple and sturdy design makes theunits suitable for continuous non-stop operation. The orbital diameter of 25mm and shaking speed of 180 RPM is standard. With DC motor for variable speed and speed regulator and digital speed meter These are heavy duty rotary shaker having stainless steel platforms and are ideal for applications demanding continuous operations CE & ISO Certified To hold 64 conical flasks of 50 ml /100 ml "Platform Size : 24""x 24"" | 1 |  |
|  | UV CABINET FOR TLC | With UV lamp - short and long wave (256 and 356 nm) Powder coated body | 1 |  |
|  | PROBE SONICATOR | Ultrasonic Power : 150 Watts Ultrasonic Frequency : 20 kHz Probe : 6 mm Processing Volume : 1 -150 ml Display : LCD Screen Programmable : 10 Nos. of program set and stored. Power Supply : AC 230V & 50/60 Hz; Single Phase. Probe Material : Titanium Alloy TI-6AL-4V Frequency Control Manual Tuning Amplitude / Power : Variable Amplitude & Power Control 0-25- 50-75-100%. | 1 |  |
|  | pH METER WITH MAGNETICSTIRRER | pH Meter with Magnetic Stirrer | 1 |  |
|  | pH METER | Digital pH meter with electrode | 1 |  |
| CATEGORY III |
|  | ELECTRONIC BALANCE | Capacity 220 gm Readability 0.001g. (1 mg): with very quick response Compact body High Stability various unit conversions Analog bar display square pan LCD display External Calibration Pan Size 100x100 mm BL 220 H is with standard small acrylic shield | 1 |  |
|  | COD REFLEX UNIT | Selectable Temperature RT +5°c to 150°c Materials, housing MS POWDER COATED Lid SS (OPTIONAL), Heating Up from 20°c to 150°c in 12 min Resolution ±0.1°c at the Pt100 stability Probe Type Pt100 A class, Selectable time 00:00 to 99:59 (hr:min), Dimension (L x W x H mm) 300 x 165 x 100 Heating block mm Aluminium 150 x 110 x 50, No. of tube holes 30 holes 16.2 mm dia x 40 mm depth, Power 750w, Power supply 230 v/50-60 Hz | 1 |  |
|  | ELECTRONIC BALANCE -4 DIGIT | Unibloc Technology with Internal Calibration Features: Touch key InternalCalibration, ISO Certified, Easy Setting, Expanded Piece Counting Function, Comparator Function, Formulation Mode, Power Saving Function, Windows Direct Communication Function, Power Lock, Should have superior technology like Unibloc for superior accuracy, response and durability, ~Capacity : 220g ~Minimum Display : 0.1 mg, ~Repeatability (Standard deviation) : ≤0.1mg, ~Linearity : ±0.2 mg, ~Stabilisation Time : Approx 3 Seconds, ~Operating Temperature and Humidity Limits :5-40°C , 20-85% 2, ~Temperature Coefficient for Sensitivity (10-30°C) : ± 2 ppm/ °C, ~Pan Size (mm) approx : ø91, ~Main Body Dimensions (mm) approx : 213(W) 356(D) 338(H), ~Main Body Weight (kg) approx : 6.0 ~Power Requirement : 12V, 1A Calibration : Internal | 1 |  |
|  | ARC SPECTRUM | Digital constant deviation spectrograph , with DigiEye and software, Insulated Arc stand , Arc lamp power supply 75V/5A with load, Copper electrodes (pair) 99% pure, Zinc electrodes (pair) 99% pure, Carbon electrodes (pair) 99% pure & Iron electrodes (pair) 99% pure | 1 |  |
|  | MICHELSON INTERFEROMETER WITH LASER | Interferometer with micrometer Laser with beam expander and Digital fringe counter | 1 |  |
|  | SOLAR CELL I-V CHARACTERISTICS | Polycrystalline solar cell-100mm, Digital dc current meter 0-2A, Digital dc voltmeter 0-20V, Light house with cooling fan, Halogen lamp & Resistance box 0.1-10Ω | 1 |  |
|  | CATHODE RAY OSCILLOSCOPE | Dual Trace – 30 MHz | 3 |  |
|  | HALL EFFECT APPARATUS | Hall effect set-up with digital milli-ammeter and milli –voltmeter, Electromagnet tapered 10K Gauss with gauss probe stand and sample stand, Electromagnet power supply with digital meter, Digital gauss meter and Semiconductor sample n-type and p-type | 1 |  |
|  | QUINCKE’S METHOD (SUSCEPTIBILITY) APPARATUS | Electromagnet tapered with gauss probe stand , Electromagnet power supply digital Quinck’s tubes & stand, Digital Travelling,Digital gauss meter & Sample | 1 |  |
|  | ULTRA-SONIC INTERFEROMETER | Export quality Spectrometer RF oscillator 3-10MHz, 250V Aqua grating Sodium vapor lamp set | 1 |  |
|  | FUNCTION GENERATOR | Frequency Range,0.01Hz TO 2 MHz,Output Impedance 50 ohms,FrequencyIndication Accuracy ±1% +1 digit, Output Waveforms- Sinusoidal, Triangle, Square, Ramp,Pulse, TTL (Sync) & DC Outputs. Sine Distortion <1% (typical).Square Wave Rise / Fall Time <75nsec. Frequency Stability <0.5% of the set frequency,Duty Cycle 10% to 90% variable | 4 |  |
| CATEGORY IV |
|  | COPLIN JAR | Soda Glass. for 5/10 Slides | 15 |  |
|  | SOXHLET EXTRACTION APPARATUS UNIT | Heating Mantles are arranged in a row. Housing is made with MS sheet duly powder coated, Supplied with two nos MS stand and one adjustable rod equipped with individual Energy Regulator and Pilot Lamp to work on 220-230 VAC:500mlx3 | 1 |  |
|  | GLASS UNITS FOR SOXHLET EXTRACTION APPARATUS | Soxhlet Extraction Apparatus Complete with allihn Condenser, Interchangeable joints Glass Parts . Complies with IS 10640 Used for separation of the extract from the liquid or solid Greater surface area than the Liebig Condenser owing to a series of bulbs, resulting in higher cooling capacity This Method enables effective separation, with relatively small quantities of solvent Idea for laboratory scale refluxing. Allihn Condenser , interchangeable Joint & Flask | 3 |  |
| CATEGORY V |
|  | STUDENT MICROSCOPE | All metal rugged Stand with individual Coarse & Fine Focus drive with focus stop Maintenance Free ECO LED illumination including Battery backup, with regulating intensity control for 220V/50Hz movable Achromatic Condenser 0.90 NA with aperture iris diaphragm, 115 X 125 mm plain stage Quadruple Revolving nosepiece Achromatic objectives 4x, 10x, 40x (spring), 360° rotatable 45° inclined Monocular head with Wide field Eyepiece 10x/18 lockable, dustcover | 2 |  |
|  | MICROSCOPE CAMERA | Magcam DC 5 Camera (with 0.5x focusable C Mount adapter) PC based USB 2.0, Colour C mos Camera For Microscopy. MagVision Software with Driversoftware, Capturing & Calibration and Measuring, Supplied with Camera , Software | 1 |  |
|  | OLYMPUS RESEARCH MICROSCOPE MODEL CX-33WITH DRAWING TUBE ATTACHMENT | Olympus Imported TrinocularMicroscope Model CX33 with universal infinitycorrected UIS2 optical System, Built in transmitted Koehler Precentered LED illumination, Co-axial coarse & fine focusing on both sides with focusing stopper & torque adjustment for coarse adjustment knob, Quadruple revolving nosepiece with inward tilt, anti fungal, Plan Achromat objectives 4X/ 0.10 W.D 27.8 mm, 10X/0.25 W.D. 8 mm, 40X/0.65 W.D. 0.6mm (spring) &100X/1.25 W.D. 0.13 mm (spring, oil), Travelling range (X × Y): 76 mm ×52mm,wiremovement,singlespecimen holder, anti fungalSiedentopf design Trinocular observation tube inclined at30° inclined having Interpupillary distance adjusting range: 48~75 mm. Widefield paired eyepiece of 10X (F.No. 22), Abbe condenser NA 1.25 with built-in aperture iris diaphragm, Power cord & dust cover. | 1 |  |
|  | DIGITAL TRAVELLING MICROSCOPE WITH DISPLAY | Travelling microscope with digital display | 1 |  |
| CATEGORY VI |
|  | MULTI PARAMETER WATER QUALITY ANALYZER | Control Â¼ C Based;Display Parameters LCD All pH Range Resolution 0- 14 0.001 Temperature 0 - 100oC; ORP mV +- 1999; Conductivity Range 0 Â¼ S -100 mS Resolution 0.1 Â¼ S TDS Salinity 0 - 1000 ppm 0 - 100 ppt DO Range Resolution Temperature-0-20 ppm 0.01 ppm0 - 50oC; Colorimeter ABS Range Concentration,Filter-400-700 nm 0 - 1.999 A0 – 1999 Set of 3 Filters Turbidity Range Principal-0-100 NTU Tyndall Effect | 1 |  |
|  | DOUBLEB BEAM UV-VISIBLE SPECTROPHOTOMETER WITH DRS ATTACHMENT | Optical Design- Double beam optical system, Spectral Bandwidths- Variable: 1.0, nm, 2.0 nm, Light Source- Xenon, 3-year lifetime guaranteed (More than 7 years typical lifetime), Detector- Dual siliconphotodiodes, Scan Ordinate Modes-Absorbance,% Transmittance,% Reflectance, Kubelka-Munk, Log (1/R),Log(Abs), Abs*Factor, Intensity (Sample Beam), Minimum Data Resolution(wavelength scanning)- 0.1 nm, Wavelength Range- 190-1100 nm, Wavelength Accuracy- ±0.80nmfor190to900nm±0.50nm(546.11 nm mercury emissionline), Wavelength Repeatability- < 0.1 nm (standarddeviation of 10 measurements), Scan Speed- 6000nm/min or better, Slew Speed-31,000nm/min or better, Data Intervals- 10, 5, 2,1, 0.5, 0.2, and 0.1 nm, Photometric Range- >3.5 A or better, Photometric DisplayRange- -0.3 to 4.0 A or better, Photometric Accuracy: Instrument- 0.5 A: ± 0.004 A 1 A: ± 0.006 A 2 A: ± 0.010 A , Photometric Accuracy: Sealed Standard Solutions- ±0.010 A (60 mg/L K2Cr2O4), Noise- 0 A: <0.00015 A 1 A: < 0.00050 A 2 A: < 0.00080A Measured at 260 nm, 1.0 nm SBW, RMS, Repeatability- 1 A: ± 0.0025 A StrayLight- 198 nm: KCl: > 1 %T 220 nm: NaI: > 0.05%T340 nm: NaNO2: > 0.05 %T, Baseline flatness- ± 0.0010 A Measured at 200-800 nm, 1.0 nm SBW, smoothing. | 1 |  |

| II Items for Networking Lab |
| --- |
| 1 | Server | Server - mini tower Server-Processor1 x Intel Xeon E3-1225V5/3.3 GHz (3.7 GHz) (Quad-Core)Processor Main Features Intel Turbo Boost Technology 2- Dell Monitor 19 inch/Dell keyboard and mouse. | 1 |  |
| 2 | DELL DESKTOP PC | INTEL CORE I 3 8TH GEN-4GB RAM-1TB HDD.-DELL MONITOR 19" INCH-WINDOWS 10 OPERATING SYSTEM DELL KEYBOARD & MOUSE | 12 |  |
| 3 | 3KVAONLINE-UPS- EXIDE 66Ah battery x 8 | 3KVA ONLINE-UPS | 1 |  |
| 4 | SERVER OS | Server OPERATING SYSTEM WINDOWS SERVER 2016 ORGINAL WITHPRDUCT KEY | 1 |  |
| 5 | ANTIVIRUS | WINDOWS 10 OPERATING SYSTEM DELL KEYBOARD & MOUSE | 13 |  |
| 6 | VALRACK | 6u 650mm d Wall mount rack with accessories. | 1 |  |
| 7 | 24 PORT GB SWITCH | Fast Ethernet:100 Mbps Half-Duplex 200 Mbps Full-Duplex Ethernet: 10 Mbps Half-Duplex 20 Mbps Full-Duplex | 1 |  |
| 8 | CABLES | Cat 6 cable | 305 mtrs |  |
| 9 | MATERIALS FOR ALL ITEMS | I O Box 24 Port 10/100/1000 Giga Switch Rack 9U Cable manager Patch panel Patch code | 28 2 1 2 2 56 |  |
| 10 | Installation | Cable laying, Installation and configuration |  |  |